## Slide 1: Logic Shift and Rotation
Reference: Assembly Language Programming and Organization of the IBM PC – Charles Marut – Chapter 7

## Slide 2: Shift

## Slide 3: Content
Introduction
Types of Shift Logical shift Shift Left Shift right
Arithmetical shift Shift arithmetic left
Shift arithmetic right
Reference

## Slide 4: Introduction
Shift operation move the bits in a pattern, changing the position of the bits. They can move bits to the left or to the right. We can divide shift operation into two categories:
1. Logical Shift
2. Arithmetic Shift

## Slide 5: Logical Shift
A logical shift moves the bits within the cell one position to the right or to the left
In a logical right shift, the least significant bit LSB is discarded and the most significant bit MSB is assigned 0.
In a logical left shift, the LSB is assigned 0 and the msb is discarded.
A shift instruction will have an operand that specifies how many times the one position shift is applied.
There are two kinds of Logical shift:
1. Shift Left
2. Shift Right

## Slide 6: Left Shift
A shift left logical of one position moves each bit to the left by one. The low-order bit LSB is replaced by a zero bit and the high-order bit MSB move to CF (Carry Flag)
Shifting by two positions is the same as performing a one-position shift two times. Shifting by zero positions leaves the pattern unchanged. Shifting an N-bit pattern left by N or more positions changes all of the bits to zero.
The picture shows the operation performed on eight bits. The original pattern is 11010011. The resulting pattern is 10100110.

## Slide 7: Right shift
A shift right logical of one position moves each bit to the right by one. The high-order bit MSB is replaced by a zero bit and the low-order bit LSB move to CF (Carry Flag)
Shifting by two positions is the same as performing a one-position shift two times. Shifting by zero positions leaves the pattern unchanged. Shifting an N-bit pattern right by N or more positions changes all of the bits to zero.
The picture shows the operation performed on eight bits. The original pattern is 00010111. The resulting pattern is 00001011.

## Slide 8: Arithmetic shift
Arithmetic shift operations assume that the bit pattern is a signed integer in two’s complement format. Arithmetic right shift is used to divide an integer by two, while arithmetic left shift is used to multiply an integer by two.
There are two kinds of arithmetic shift:
1. Left arithmetic shift
2. Right arithmetic shift

## Slide 9: Left Arithmetic shift
An shift arithmetic left is the same as a logical left shift
A shift arithmetic left of one position moves each bit to the left by one. The low-order bit LSB is replaced by a zero bit and the high-order bit MSB move to CF (Carry Flag)
A left arithmetic shift by n is equivalent to multiplying by 2n . In 2’s complement, positive or negative, a logical left shift, is equivalent to multiplication by two.
The picture shows the operation performed on eight bits. The original pattern is 11010011. The resulting pattern is 10100110.

## Slide 10: Shift Arithmetic Right
A shift arithmetic right of one position moves each bit to the right by one. The high-order bit MSB is replaced by sign bit and the low-order bit LSB move to CF (Carry Flag)
A shift arithmetic right is equivalent to integer division by two.
In 2’s complement, positive or negative, division by two is accomplished via an shift arithmetic right .
The picture shows the operation performed on eight bits. The original pattern is 00010111. The resulting pattern is 00001011

## Slide 11: Rotation

## Slide 12: Contents
Types of Rotation
ROL Instruction
ROR Instruction
Difference
RCL Instruction
RCR Instruction

## Slide 13: Types
Rotation
ROL
ROR
RCL
RCR

## Slide 14: ROL Instruction
ROL (rotate) shifts each bit to the left
The highest bit is copied into both the Carry flag and into the lowest bit
No bits are lost
ROL is used for unsigned data

## Slide 15
Below are instances of the ROL instruction :
 |  | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1
BH
1
2
3
1
1 |  | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1
1
1
2
3
1 |  | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1
011
011
CF

## Slide 16: ROR Instruction
ROR (rotate right) shifts each bit to the right
The lowest bit is copied into both the Carry flag and into the highest bit
No bits are lost
ROR is for unsigned data

## Slide 17
A few examples on ROR:
1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 |  | 
BH
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 |  | 1
0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 |  | 0
011
1
011
1
2
3
1
2
3
CF

## Slide 18: RCL Instruction
RCL (rotate carry left) shifts each bit to the left
Copies the Carry flag to the least significant bit
Copies the most significant bit to the Carry flag
RCL is for signed data

## Slide 19: Example:
CLC ; CF = 0
MOV BL,88H ; CF,BL = 0 10001000B
RCL BL,1 ; CF,BL = 1 00010000B
RCL BL,1 ; CF,BL = 0 00100001b
0 |  | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
BL
1 |  | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 |  | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
1
0
CF

## Slide 20: RCR Instruction
RCR (rotate carry right) shifts each bit to the right
Copies the Carry flag to the most significant bit
Copies the least significant bit to the Carry flag

## Slide 21: Example:
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 |  | 1
AH
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |  | 0
1
STC ; CF = 1
MOV AH,10H ; CF,AH = 00010000 1
RCR AH,1 ; CF,AH = 10001000 0
CF

## Slide 22: Difference
The difference between ROR and RCR is only the way of operation. In RCR, every bit that is rotated will enter the carry flag before entering the leftmost bit
RCL works like just like ROL except that CF is part of the circle of bits being rotated.

## Slide 23
The End